| 1. GENERAL DATA |
| --- |
| PROJECT NAME: | PROJECT NO.: |
| WC P.O. / CONTRACT NO.: | LINE / ITEM NO.: |
| 2. TRANSFORMER DATA |
| MAKE: | MODEL: |
| SERIAL NO.: | INSULATION CLASS: |
| ENCLOSURE PROTECTION: IP___ | CAPACITOR CONNECTION: |
| SYSTEM VOLTAGE: | CT RATIO: |
| RATING(Total KVAR): | FREQUENCY: |
| CAPACITOR VOLTAGE: | RATED CURRENT: |
| MF DWG NO.(S): | WC DWG NO.: |

| 3. INSPECTION | DONE /YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| 1 | Confirm LV circuit breaker trip settings are as per manufacturer and/or WC protection requirements |  |  |  |  |
| 2 | Megger phase to phase and phase to earth. Confirm acceptable |  |  |  |  |
| 3 | Confirm LV power cables pre-commissioned separately |  |  |  |  |
| 4 | Confirm arc flash system tested and operational |  |  |  |  |
| 5 | Confirm all covers installed and PFC safe to energise |  |  |  |  |
| 6 | Confirm required settings programmed |  |  |  |  |
| 7 | Energise PFC no-load for 2 hours. Confirm acceptable |  |  |  |  |
| 8 | Energise PFC with different stages of load for 2 hours Confirm PF controlled to setpoint |  |  |  |  |
| 9 | Confirm temperature rise acceptable |  |  |  |  |
| 10 | Record primary voltage and current – confirm acceptable |  |  |  |  |
| 11 | Confirm low PF alarm operates |  |  |  |  |
| 12 | Confirm settings loaded to MDT autosave |  |  |  |  |

4. REMARKS / REMEDIAL ACTIONS

| 5. TESTS |
| --- |
| 5.1 Test Equipment |
| Megger |
| Manufacturer: | Model: |
| Serial No.: | Last Calibration Date: |
| Multimeter |
| Manufacturer: | Model: |
| Serial No.: | Last Calibration Date: |
| 5.2 Insulation Resistance Test |
| Circuit Description | L1-L2 (__kV) | L2-L3 (__kV) | L3-L1 (__kV)) | L1-E (__kV) | L2-E (__kV) | L3-E (__kV) |
| Resistance (Ω) |  |  |  |  |  |  |
| 5.3 Power factor measurement |
| Description | Voltage(V) | Current(A) | System PF(Lag) |  |
| Motor no.1(________KW) |  |  |  |  |
| Motor no.1+Motor no.2(________KW) |  |  |  |  |
| Motor no.1+Motor no.2+Motor no.3 (________KW) |  |  |  |  |

| 6. SIGNOFFS |  |
| --- | --- |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |