- All ITR documents to be completed & witnessed by competent person/s

- Compliance to be achieved to contract requirements and all latest versions of applicable standards

| 1. REFERENCE INFORMATION |
| --- |
| INSPECTION DATA | ASSET DATA |
| PROJECT NAME: | MANUFACTURER: |
| LOCATION: | MF SERIAL NO: |
| INSPECTION DATE: | WC FLER / TAG NO: |
| INSPECTOR NAME: | TYPE / MODEL NO / SIZE: |
| PROJECT / CONTRACT NO: | DESIGN CRITERIA: |
| ATTENDEES: |

| 2. INSPECTION PREPARATION |
| --- |
|  | OSH compliance requirements. |
|  | Obtain QA / QC documentation (review outstanding items). |
|  | Relevant Water Corporation standards. |
|  | Relevant Australian Standards. |
|  | Supporting contract documentation / approved drawings. |
|  | Provision of required test equipment. |
|  | Provision of required test reports. |

*Contents of Section 3 (Inspection) and Section 4 (Test) are Asset Specific and shall reflect relevant SPS / Australian Standard(s) where practicable. Entries shall also be worded to reflect the procedures involved in a step-by-step manner; i.e. “Conduct visual inspection and ensure pre-start photographs are taken”, “Extract bearing housing covers to expose bearings and full shaft length”.

| 3. INSPECTION & 4. TESTING | YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| GENERAL |
| 1 | Hoist or chain block and beam capacity as per specification? |  |  |  | Capacity: _________ kg/tonnes Monorail/Beam: ___________ mm |
| 2 | Monorail inspected by a competent person prior to loading or operation? |  |  |  | Attach signed off inspection check sheet to this ITR. |
| 3 | Monorail installed in correct location per drawings? |  |  |  |  |
| ERECTION |
| Erection checked as part of inspection to ensure that: |  |  |  |  |
| 4 | - erection tolerance in accordance with AS 1418.1 and AS1418.18? |  |  |  |  |
| 5 | - monorail beam is level and aligned? |  |  |  | Cert to be supplied for the alignment |
| 6 | - height of monorail beam adjusted (if required for levelling) using shims and packers in accordance with DS 30-02? |  |  |  |  |
| 7 | - weld quality acceptable if a fabricated beam or welded gussets are adopted? |  |  |  | Ensure a qualified welding inspector has been consulted. Note incorrect weld procedures can lead to distortion of beam thus affecting alignment and capacity rating. |
| 8 | - bolt and washer sizes, materials and grades correct for fastening of beam to supports ? |  |  |  |  |
| 9 | - bolt torques correct? |  |  |  |  |
| END STOPS |
| End of monorail beam checked as part of inspection to ensure that: |  |  |  |  |
| 10 | - buffers installed, secure and in good condition? |  |  |  |  |
| 11 | - fail-safe, self-resetting, automatic and positive motion travel limiting devices installed and at correct location? |  |  |  |  |
| 12 | - travel limit devices accessible from crane service platform? |  |  |  |  |
| ACCESS PLATFORM |
| Inspection of the monorail access platform completed (if applicable), including checks of: |  |  |  |  |
| 13 | - correct platform position per drawing? |  |  |  |  |
| 14 | - acceptability of access to and around the platform (ref. Australian Standards) relating to handrails, ladders, grid meshing/flooring? |  |  |  |  |
| 15 | - confirm a 240 VAC, 10 amp single-phase socket outlet provided at a convenient location for maintenance purposes? |  |  |  |  |
| TROLLEY |
| Trolley checked as part of inspection, including checks for: |  |  |  |  |
| 16 | - correct trolley drive details/ratings? |  |  |  |  |
| 17 | - lubrication and oil levels? |  |  |  |  |
| 18 | - trolley wheels/bogies being secure and turning freely without squealing |  |  |  |  |
| LIFTING GEAR |
| Lifting gear ( electric hoist or chain block) inspected as part of inspection, including checks on: |  |  |  |  |
| 19 | - lifting chain rating and condition? |  |  |  |  |
| 20 | - wire rope rating and condition? |  |  |  |  |
| 21 | - lifting hook rating and condition? |  |  |  |  |
| 22 | - hook fitted with safety latch? |  |  |  |  |
| PENDANT AND CONTROLS OR CHAIN |
| Accessibility of pendant and controls checked as part of inspection, including: |  |  |  |  |
| 23 | - acceptability of pendant height above floor? (1.0 to 1.2m) |  |  |  |  |
| 24 | - access to pendant throughout length of building? |  |  |  |  |
| 25 | - pendant freely movable along rail and independent from hoist? |  |  |  |  |
| 26 | - confirm pendant suspended in such a manner that it is capable of supporting a 90kg person? |  |  |  |  |
| 27 | - chain length reaches operable level from floor ? |  |  |  | Applicable to chain block driven trolleys and lifting gear |
| SURFACE PROTECTION |
| Structural steelwork coating checked as part of inspection, including detection of: |  |  |  |  |
| 28 | - coating defects? |  |  |  |  |
| 29 | - unacceptably low DFT? |  |  |  |  |
| SAFETY AND SIGNAGE |
| Safety and signage checks completed as part of inspection, including: |  |  |  |  |
| 29 | - correct SWL labelling? |  |  |  |  |
| 30 | - Worksafe registration number clearly visible? |  |  |  |  |
| 31 | - FL number clearly visible? |  |  |  |  |
| 32 | - N-S-E-W direction of movement labelling? |  |  |  |  |
| 33 | - appropriateness of danger and warning signs (and their locations)? |  |  |  |  |
| 34 | - provision of safety guards? |  |  |  |  |
| 35 | - confirm crane power isolator installed |  |  |  |  |

*Contents of Section 5 to be retained where applicable; i.e. if coatings inspection is required. Sections 6 & 7 to be retained in all ITRs.

| 5. COATINGS INSPECTION | YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| 1 | Check that asset external coating is free of damage |  |  |  | Repair if required according to coating manufacturers recommendation |

| 6. REMARKS / REMEDIAL / FOLLOW UP ACTIONS | ACTION BY | TARGET DATE | STATUS |
| --- | --- | --- | --- |

| 7. SIGNOFFS |
| --- |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |