- All ITR documents to be completed & witnessed by competent person/s

- Compliance to be achieved to contract requirements and all latest versions of applicable standards

| 1. REFERENCE INFORMATION |
| --- |
| INSPECTION DATA | ASSET DATA |
| PROJECT NAME: | MANUFACTURER: |
| LOCATION: | MF SERIAL NO: |
| INSPECTION DATE: | WC FLER / TAG NO: |
| INSPECTOR NAME: | TYPE / MODEL NO / SIZE: |
| PROJECT / CONTRACT NO: | DESIGN CRITERIA: |
| ATTENDEES: |

| 2. INSPECTION PREPARATION |
| --- |
|  | OSH compliance requirements. |
|  | Obtain QA / QC documentation (review outstanding items). |
|  | Relevant Water Corporation standards. |
|  | Relevant Australian Standards. |
|  | Supporting contract documentation / approved drawings. |
|  | Provision of required test equipment. |
|  | Provision of required test reports and certificates; i.e. hydrostatic test, material certificates, etc. |

| 3. INSPECTION | YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| GENERAL |
| 1 | Confirm if O&M Manuals have been provided (hardcopy / softcopy) |  |  |  | Hardcopy / softcopy? (please circle) |
| 2 | Conduct visual inspection, and ensure photographs are taken |  |  |  |  |
| MATERIALS AND ARRANGEMENT |
| 2 | Verify construction materials with material certificates, specification, and relevant drawings |  |  |  |  |
| 3 | Confirm major dimensions correct per drawing |  |  |  | Attach a copy of the clarifier drawing(s) to this record sheet highlighting on the drawing which dimensions were checked. |
|  | Influent Pipe Connection |  |  |  |  |
| 4 | Flange standard correct |  |  |  | Flange face: FF / RF |
| 5 | Diameter correct |  |  |  | Class: |
| 6 | Pitch circle diameter correct |  |  |  | PCD: __________mm |
| 7 | Number and diameter of bolt holes correct? |  |  |  | No.: _______ Dia.: _________mm |
|  | Draft Tube/Support Column and Shroud |  |  |  |  |
| 8 | Verify draft tube is correct type (as per design) |  |  |  | Dia.: _________mm |
|  | Verify shroud is correct type (as per design) |  |  |  | Dia.: _________mm |
| 9 | Verify all components are present |  |  |  |  |
|  | Stilling/Feed Well Assembly |  |  |  |  |
| 10 | Verify stilling/feed well is correct type (as per design) |  |  |  |  |
| 11 | Verify all components are present |  |  |  |  |
|  | Bridge/Gated Walkway |  |  |  |  |
| 12 | Verify bridge is correct type (as per design) |  |  |  |  |
| 13 | Verify all components are present |  |  |  |  |
|  | Slew Bearing Assembly (if applicable) |  |  |  |  |
| 14 | Verify slewing assembly is correct type (as per design) |  |  |  |  |
| 15 | Verify correct components are present |  |  |  |  |
|  | Drive and Motor Assembly |  |  |  |  |
| 16 | Verify motor is correct type (as per design) |  |  |  | kW: _______ |
| 17 | Verify gearbox is correct type |  |  |  |  |
| 18 | Verify all components are present |  |  |  |  |
|  | Top Rake or Scum Skimmer Arm Assembly |  |  |  |  |
| 19 | Verify rake is correct type (as per design) |  |  |  | No. of arms: _______ |
| 20 | Verify all beach/effluent trough components are present |  |  |  |  |
| 21 | Verify all rake components are present |  |  |  |  |
|  | Launder Assembly (if applicable) |  |  |  |  |
| 22 | Verify launders/weirs are the correct type (as per design) |  |  |  |  |
| 23 | Verify all components are present (including scum baffle, if applicable) |  |  |  |  |
|  | Bottom Rake or Sludge Collector Arm or Suction Header Assembly |  |  |  |  |
| 24 | Verify rake and support is correct type (as per design) |  |  |  | No. of arms: _______ |
| 25 | Verify all rake support components are present |  |  |  |  |
| 26 | Verify rake counterbalance arm is present (if applicable) |  |  |  |  |
| 27 | Verify all rake components are present |  |  |  |  |
|  | Cathodic Protection (if applicable) |  |  |  |  |
| 28 | Verify all components are present |  |  |  |  |

| 4. REMARKS / REMEDIAL / FOLLOW UP ACTIONS | ACTION BY | TARGET DATE | STATUS |
| --- | --- | --- | --- |

| 5. SIGNOFFS |
| --- |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |

POST TRANSPORTATION INSPECTION

- Inspection to be completed at point of delivery

- If a supply verification was not completed at the manufacturer, both supply verification and post transportation inspection should be completed at point of delivery.

| 6. POST TRANSPORTATION REMARKS / REMEDIAL / FOLLOW UP ACTIONS | ACTION BY | TARGET DATE |
| --- | --- | --- |

| 7. SIGNOFFS |
| --- |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |