| All ITR documents to be completed & witnessed by competent person/s Compliance to be achieved to contract requirements and all latest versions of applicable standards |
| --- |
| 1. REFERENCE INFORMATION |
| INSPECTION DATA | ASSET DATA |
| PROJECT NAME: | MANUFACTURER: |
| LOCATION: | INSPECTION DATE |
| INSPECTOR NAME: |  |
| PROJECT / CONTRACT NO: | DESIGN CRITERIA: |
| ATTENDEES: |

| 2. INSPECTION PREPARATION |
| --- |
|  | OSH compliance requirements. |
|  | Obtain QA / QC documentation (review outstanding items). |
|  | Relevant Water Corporation standards. |
|  | Relevant Australian Standards. |
|  | Supporting contract documentation / approved drawings. |
|  | Provision of required test equipment. |
|  | Provision of required test reports and certificates; i.e. hydrostatic test, material certificates, etc. |

*Contents of Section 3 (Inspection) and Section 4 (Test) are Asset Specific and shall reflect relevant SPS / Australian Standard(s) where practicable. Entries shall also be worded to reflect the procedures involved in a step-by-step manner; i.e. “Conduct visual inspection and ensure pre-start photographs are taken”, “Extract bearing housing covers to expose bearings and full shaft length”.

| 3. INSPECTION | YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| GENERAL |
| 1 | Confirm major dimensions correct as per drawing |  |  |  | Attach a copy of the aerator drawing to this record sheet highlighting on the drawing which dimensions were checked. |
| 2 | Confirm spray nozzles are installed securely in header and equally spaced according to drawings |  |  |  |  |
| 3 | Confirm floor is sloped to the outlet to the gradient detailed in drawings |  |  |  |  |
| 4 | Confirm the appropriate concrete floor sealing has been applied according to specification and drawings |  |  |  |  |
| 5 | Confirm internal ladders, grid meshing flooring, walkways, stairs are secure and comply with Australian Standards AS1657 and S151? |  |  |  |  |
| 6 | Check wall sheeting is securely fastened to support structure |  |  |  |  |
| 7 | Confirm wall support structure is securely bolted to foundation with appropriate grouting where applicable |  |  |  |  |
| 8 | Confirm aerator headers are supported and secured adequately to prevent deflection between supports |  |  |  |  |
| 9 | For PVC internal headers ensure cracks are not evident especially on threaded fittings |  |  |  |  |
| 10 | Verify gasket material and thickness for all piping flanged connections |  |  |  | Material: CMF EPDM Other _____________________ Thickness: _________________mm |
| 11 | Confirm all flange bolts and nuts are installed and that bolt sizes, material and grade are correct |  |  |  | Size: ________ Material: __________ Grade: 4.6 8.8 Other: _______ |
| 12 | Confirm correct protrusion of bolt threads past nut |  |  |  | Protrusion: _____________________ |
| 13 | Confirm correct bolt tightening sequence has been followed |  |  |  |  |
| 14 | Verify bolt torque requirements comply with DS-38. Also verify actual bolt torque applied to each bolt is correct |  |  |  | DS38 bolt torque: _____________Nm Actual bolt torque: _____________Nm |
| 15 | If required by design, verify that flange isolation materials have been installed correctly |  |  |  |  |
| 16 | Confirm the control valves are adequately supported |  |  |  |  |
| 17 | Confirm whether a pressure transmitter on inlet pipework has been installed securely and to manufacturer’s recommendations |  |  |  |  |

| 4. TEST | PASS | FAIL | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| 1 | Not applicable |  |  |  |  |

*Contents of Section 5 to be retained where applicable; i.e. if coatings inspection is required. Sections 6 - 9 to be retained in all ITR’s.

| 5. COATINGS INSPECTION | YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| 1 | Check that pipework and support structure internal coating is free of damage |  |  |  |  |
| 2 | Check that pipework and support structure external coating is free of damage |  |  |  |  |

| 6. REMARKS / REMEDIAL / FOLLOW UP ACTIONS | ACTION BY | TARGET DATE | STATUS |
| --- | --- | --- | --- |

| 7. SIGNOFFS |
| --- |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |