| All ITR documents to be completed & witnessed by competent person/s Compliance to be achieved to contract requirements and all latest versions of applicable standards |
| --- |
| 1. REFERENCE INFORMATION |
| INSPECTION DATA | ASSET DATA |
| PROJECT NAME: | MANUFACTURER: |
| LOCATION: | MF SERIAL NO: |
| INSPECTION DATE: | WC FLER / TAG NO: |
| INSPECTOR NAME: | TYPE / MODEL NO / SIZE: |
| PROJECT / CONTRACT NO: | DESIGN CRITERIA: |
| ATTENDEES: |

| 2. INSPECTION PREPARATION |
| --- |
|  | OSH compliance requirements. |
|  | Obtain QA / QC documentation (review outstanding items). |
|  | Relevant Water Corporation standards. |
|  | Relevant Australian Standards. |
|  | Supporting contract documentation / approved drawings. |
|  | Provision of required test equipment. |
|  | Provision of required test reports. |
|  | Prepare application form 101 for hazard level A, B or C vessels |

*Contents of Section 3 (Inspection) and Section 4 (Test) are Asset Specific and shall reflect relevant SPS / Australian Standard(s) where practicable. Entries shall also be worded to reflect the procedures involved in a step-by-step manner; i.e. “Conduct visual inspection and ensure pre-start photographs are taken”, “Extract bearing housing covers to expose bearings and full shaft length”.

| 3. INSPECTION & 4. TESTING | YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| GENERAL |
| 1 | Locate and verify that name plate/label details match specification and contract requirements |  |  |  | Check: Make/Model/Connection size/Serial number/ Design Standard/Volume/Internal Diameter / Operating Fluid/Design Pressure/Hazard Level / Year of Manufacture etc |
| 2 | Multi-media vessel installed in correct location as per drawings? |  |  |  |  |
| 3 | Orientation of vessel correct? |  |  |  |  |
| 4 | Vessel installed per manufacturer’s recommendations? |  |  |  |  |
| 5a | Confirm the vessel design has been registered with an Australian regulatory authority and the design registration number is present on the name plate. |  |  |  |  |
| 5b | For hazard level A, B or C vessels, perform commissioning inspection and submit application form 101 for plant registration |  |  |  |  |
| 5c | Where applicable place a copy of the plant registration on or near the vessel and stamp plant registration number on the nameplate or the vessel |  |  |  |  |
| 6 | Confirm if the vessel installer has compiled a punch list and ensure all items are complete? |  |  |  |  |
| 7 | Confirm correct type of air valve has been installed on each vessel |  |  |  |  |
| 8 | Confirm correctly rated pressure relief valve has been installed on each vessel |  |  |  |  |
| LEVELLING AND ALIGNMENT OF VESSEL |
| 9 | Multi-media vessel plumb and level? |  |  |  |  |
| 10 | Multi-media vessel aligned to pipe work? |  |  |  |  |
| 11 | Gap between base-ring and foundation adequate for grouting? |  |  |  | Gap: _________________ mm |
| 12 | Correct type of grout used for base-ring? |  |  |  | Grout:_____________________ |
| 13 | Grout adequately distributed and free of voids? |  |  |  |  |
| 14 | Holes / gaps provided in grout (or gasket) for drainage? |  |  |  |  |
| 15 | Foundation bolts size, material and grade correct? |  |  |  | Size: _______ Material:______________ Grade: _______________ |
| 16 | Foundation bolts tightened? |  |  |  |  |
| 17 | Correct protrusion of foundation bolt threads past nut? |  |  |  | No. of Threads: _______ |
| INLET / OUTLET NOZZLE BOLT-UP |
| 17 | Mating flanges flat, clean and free of irregularities? |  |  |  |  |
| 18 | Gasket material and thickness correct? |  |  |  | Material: CMF EPDM Other______ Thickness: ____________ mm |
| 19 | Bolt size, material and grade correct? |  |  |  | Size: _______ Material:_____________ Grade: 4.6 8.8 Other_________ |
| 20 | Correct protrusion of bolt threads past nut? |  |  |  |  |
| 21 | Correct bolt tightening sequence followed? |  |  |  |  |
| 22 | Final bolt torques correct? |  |  |  | Torque: __________________ Nm |
| MANHOLE BOLT-UP |
| 23 | Mating flanges flat, clean and free of irregularities? |  |  |  |  |
| 24 | Gasket material and thickness correct? |  |  |  | Material: CMF EPDM Other______ Thickness: ____________ mm |
| 25 | Bolt size, material and grade correct? |  |  |  | Size: _______ Material:_____________ Grade: 4.6 8.8 Other_________ |
| 26 | Correct protrusion of bolt threads past nut? |  |  |  |  |
| 27 | Correct bolt tightening sequence followed? |  |  |  |  |
| 28 | Final bolt torques correct? |  |  |  | Torque: __________________ Nm |
| 29 | Correct fasteners utilised? |  |  |  |  |
| EXTERNAL INSPECTION |
| 30 | External coating / surface free of damage caused during transport / installation? |  |  |  |  |
| 31 | Earthing strap installed and secure? |  |  |  |  |
| 32 | Confirm that the access ways comply with AS1657 and WC SPS151 |  |  |  |  |

| 5. COATINGS INSPECTION | YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| 33 | Check that asset external coating is free of damage. |  |  |  | Repair if required according to coating manufacturers recommendation |

| 6. REMARKS / REMEDIAL / FOLLOW UP ACTIONS | ACTION BY | TARGET DATE | STATUS |
| --- | --- | --- | --- |

| 7. SIGNOFFS |
| --- |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |