| All ITR documents to be completed & witnessed by competent person/s Compliance to be achieved to contract requirements and all latest versions of applicable standards |
| --- |
| 1. REFERENCE INFORMATION |
| INSPECTION DATA | ASSET DATA |
| PROJECT NAME: | MANUFACTURER: |
| LOCATION: | INSPECTION DATE |
| INSPECTOR NAME: |  |
| PROJECT / CONTRACT NO: | DESIGN CRITERIA: AS1657 / DS100 |
| ATTENDEES: |

| 2. INSPECTION PREPARATION |
| --- |
|  | OSH compliance requirements. |
|  | Obtain QA / QC documentation (review outstanding items). |
|  | Relevant Water Corporation standards – see #2141010 Grid Mesh Assessment Guideline |
|  | Relevant Australian Standards. |
|  | Supporting contract documentation / approved drawings. |
|  | Provision of required test equipment. |
|  | Provision of required test reports and certificates; i.e. hydrostatic test, material certificates, etc. |

| 3. INSPECTION | YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| CONSTRUCTION |
| 1 | Material - galvanised steel, aluminium or fibre reinforced plastic (FRP) |  |  |  |  |
| 2 | Mesh type (see types on Fig 1,2,3 below) |  |  |  | Type:___________________ |
| 3 | Shape – rectangular or close to rectangular. |  |  |  |  |
| 4 | Support is under the ends of the load bars or long way mesh – Figure 4 over at least 80% of the length of each of two opposite ends – Figure 5 No overhangs (ends supported) The load bar ends have at least 25mm bearing on their supports (40mm for load bars >40mm deep, 30mm for expanded metal mesh, 40mm for FRP grid mesh load bars) - Figures 6 & 7 |  |  |  |  |
| 5 | Panel size is no less than 0.6m2 in area (eg 600mm x 1m, 800mm x 800mm, 1.5m x 400mm) |  |  |  |  |
| 6 | Span no greater than shown in the tables (Figure 15, 16 & 17 below) |  |  |  | Max span (m):_______________ |
| 7 | Fixing (state which) physically restrained by surrounds such as walls, floors, , or by locating lugs welded to the panel (Figures 10 & 11) OR Fixings, location and spacing of Grid Mesh Flooring provide at least: One fixing at each corner no farther than 200mm from the corner. Four fixings per square metre of panel for panel spans equal to or greater than one metre; Six fixings per square metre for panel less than one metre; Fixings generally spaced no farther apart than 600 mm. OR Expanded metal mesh welded every fourth strand (Figure 12) |  |  |  | Fixing type(s): ________________ |
| 8 | Fixings do support any vertical load (upwards or downwards). Expanded metal mesh panels butt welded to, or overlap one full mesh with, adjacent panels on short way side (Figures 13 & 14) |  |  |  |  |
| 9 | Other openings in panel – no greater than 40mm wide and 5000mm2 area (eg 40mm x 125mm, 20mm x 250mm) |  |  |  |  |
| INSTALLATION |
| 10 | Panels correctly positioned on its supports |  |  |  |  |
| 11 | Fixings are correctly positioned and installed in a manner which retains the panel in its intended position |  |  |  |  |
| 12 | There are adequate fixings in place |  |  |  |  |
| 13 | Fixings are tight and at 900 to supports |  |  |  |  |
| CONDITION |
| 14 | Panel not bent indicating overloading – no visible bending. Service deflection at the centre of a panel under design live loading shall not exceed- 5mm for steel, FRP gridmesh or Raised Expanded Metal mesh flooring 10mm for Chequer plate flooring |  |  |  |  |
| 15 | Load bars not twisted along their length |  |  |  |  |
| 16 | Panel is not twisted such that it does not sit properly on its supports |  |  |  |  |
| 17 | Corrosion - no significant pitting corrosion on the mesh, its supports or the fixings of the supports |  |  |  |  |
| 18 | FRP panels have no exposed glass fibres and no obvious cracks to the resin |  |  |  |  |
| 19 | Retaining fixings not bent and correctly engaging the mesh |  |  |  |  |
| 20 | Verify that bonding link(s) have been installed correctly |  |  |  |  |
| 21 | Check for these hazards (do not constitute a non-compliance with the Guidelines.) Maximum gap of 10mm to adjacent panels Adjacent panels at same level – no tripping hazard Cut outs in panels – Figure 7 overleaf no sharp edges banding bars 5 mm thick welded to the cut ends (Figures 8 & 9) no gaps greater than 40mm wide) without toe-boarding (Figure 8) |  |  |  |  |
| 22 | Guardrail Stanchion centres not to exceed 2000mm.-Figure 18 |  |  |  |  |
| 23 | Guardrail Enclosure Bend length 300mm or less.-Figure 18 |  |  |  |  |
| 24 | Distance between guardrail enclosure bends 100mm or less-Figure 18 |  |  |  |  |
| 25 | Gap between grid mesh and toe boarding 10mm or less – Figure 18 |  |  |  |  |

| 4. REMARKS / REMEDIAL / FOLLOW UP ACTIONS | ACTION BY | TARGET DATE | STATUS |
| --- | --- | --- | --- |
| . |  |  |  |

| 5. SIGNOFFS |
| --- |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |

Figure 1					Figure 2

Figure 4						Figure 5

Figure 6						Figure 7

Figure 9

Reference Table for Span between Supports - Steel and Aluminium Grid Mesh Panels

Figure 15

| Load Bar Cross Section mm | Maximum span in mm for load bars at 30mm spacing | Maximum span in mm for load bars at 40mm spacing |
| --- | --- | --- |
|  | Steel | Aluminium | Steel | Aluminium |
| 25 x 3 | 1200 | 950 | 1100 | 800 |
| 32 x 3 | 1500 | 1100 | 1400 | 950 |
| 25 x 5 | 1300 | 1100 | 1200 | 900 |
| 32 x 5 | 1600 | 1300 | 1500 | 1100 |
| 40 x 5 | 1900 | 1500 | 1750 | 1300 |
| 45 x 5 | 2100 | 1700 | 1900 | 1400 |
| 50 x 5 | 2300 | 1800 | 2100 | 1500 |

Reference Table for Span between Supports - FRP Grid Mesh Panels

Figure 16

| Load Bar Cross Section mm | Maximum span in mm for load bars at 38mm spacing |
| --- | --- |
| 25 x 6 | 750 |
| 38 x 6 | 1050 |

Reference Tables for Span between Supports – Expanded Metal Mesh Panels

Figure 17

| Nominal Mesh Size mm SWM x LWM | Strand Measurement | Maximum Span mm |  |
| --- | --- | --- | --- |
|  | Thickness mm | Width mm | Steel | Aluminium |  |
| 45 x 135 | 5 | 8 | 600 | 500 |  |
| 45 x 135 | 5 | 11 | 750 | 600 |  |
| 34 x120 | 5 | 6.4 | 750 | 550 |  |
| 34 x120 | 5 | 8.4 | 900 | 650 |  |
| 34 x120 | 5 | 9.6 | 1000 | 750 |  |
| 34 x120 | 6 | 10.4 | 1100 | 800 |  |
| 30 x 75 | 5 | 7.5 | 800 | 550 |  |
| 30 x 75 | 5 | 10.5 | 1000 | 750 |  |
| 30 x 75 | 6 | 11.0 | N/A | 800 |  |
| 25 x 60 | 5 | 5.6 | 600 | N/A |  |

Note: Other sizes of expanded metal mesh are generally not suitable for walkways but are designed for security or decorative applications. If mesh is other than one of the sizes listed above refer for detailed assessment.

Require Compliance to latest version AS1657

# Text boxes

Long Way Mesh (LWM)

Figure 3

Short Way Mesh (SWM)

End/corner unsupported

25mm minimum for load bars 25 - 40mm deep

40mm minimum for load bars 45 - 65mm deep

Figure 8

Maximum gap of 40mm without toe-boarding

Banding bar 5mm thick

Figure 11

Figure 10

Panel fitted with welded locating lugs which protrude below panel and bear against support

Panels restrained by kick plate fixed to support, adjacent concrete floor and handrail stanchion base plates

Welded every 4th Strand

Figure 13

Figure 12

Welded every 4th strand

Butt welded

Figure 14

Figure 12

Overlap one full mesh

Figure 18