| All ITR documents to be completed & witnessed by competent person/s Compliance to be achieved to contract requirements and all latest versions of applicable standards |
| --- |
| 1. REFERENCE INFORMATION |
| INSPECTION DATA | ASSET DATA |
| PROJECT NAME: | MANUFACTURER: |
| LOCATION: | MF SERIAL NO: |
| INSPECTION DATE: | WC FLER / TAG NO: |
| INSPECTOR NAME: | TYPE / MODEL NO / SIZE: |
| PROJECT / CONTRACT NO: | DESIGN CRITERIA: |
| ATTENDEES: |

| 2. INSPECTION PREPARATION |
| --- |
|  | OSH compliance requirements. |
|  | Obtain QA / QC documentation (review outstanding items). |
|  | Relevant Water Corporation standards. |
|  | Relevant Australian Standards. |
|  | Supporting contract documentation / approved drawings. |
|  | Provision of required test equipment. |
|  | Provision of required test reports and certificates; i.e. hydrostatic test, material certificates, etc. |

| 3. INSPECTION | YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| GENERAL |
| 1 | Locate and verify that name plate details match valve specification |  |  |  |  |
| 2 | Confirm that underground valves, spindles and actuators are identically numbered. |  |  |  | Verify that a Stainless Steel number tag has been installed to each. |
| 3 | Inspect and confirm valve actuator type and spindle drive |  |  |  | Actuator: Electric / Manual/ Pneumatic Spindle drive: Geared / Direct |
| 4 | Confirm valve type and seating type is correct as specified and according to expected service |  |  |  | Valve type: Knife, Metal or Resilient Seat |
| 5 | Confirm if O&M Manuals have been provided (hardcopy / softcopy) |  |  |  | Hardcopy / softcopy? (please circle) |
| 6 | Confirm that any special tools required to operate the valve have been provided if ordered from the manufacturer |  |  |  |  |
| 7 | Check that flange faces, threaded or lugged holes are clean and are free from any defects resulting from corrosion or any other causes |  |  |  |  |
| 8 | Inspect valve to ensure equipment is adequately clean |  |  |  |  |
| MATERIALS AND ARRANGEMENT |
| 9 | Verify construction materials (refer to valve name plate) with specifications, SPS and relevant drawings. Note different SPS’s are applicable depending on type of gate valve. Classification of service will also govern materials of construction. |  |  |  |  |
| 10 | For highly corrosive service applications is the valve suitably bonneted for protection of gate, spindle and gland box |  |  |  |  |
| 11 | Measure face to face length of valve and verify correct length with manufacturer dimensions or general arrangement drawing(s). |  |  |  | Length: Checked against: MF Dimensions / G.A. Dwg |
| 12 | Confirm flange details on name plate match specifications and SPS requirements |  |  |  | Flange Aust. Standard: Flange Type: Wafer or Lugged Flange Size: Flange Class: |
| 13 | For highly corrosive service applications are the flanges suitably lugged |  |  |  |  |
| 14 | For highly corrosive service applications is the packing/sealing material suitable (PTFE/Viton) |  |  |  |  |
| 15 | Measure pitch circle diameter of valve and verify with specification / relevant Standards |  |  |  | PCD: |
| 16 | Count number of bolt holes and measure bolt hole diameters. Verify number and diameter lengths with specification / relevant Standards |  |  |  | No.: Dia: |
| 17 | Count number of threaded holes and measure bolt hole diameters. Verify number and diameter lengths with specification / relevant Standards |  |  |  | No.: Dia: |
| 18 | Measure distance from centreline of valve to top of cap / hand-wheel and verify with specification |  |  |  | Distance(mm): |
| 19 | For buried or submersible sewage applications is the valve supplied with square spindle cap to suit extension spindle and tube? |  |  |  |  |
| 20 | Is the extension spindle and tube of suitable length for the buried and submersible sewage application? |  |  |  |  |
| 21 | For metal and resilient seated valves on waterworks ensure a gearbox is installed when closing against flow |  |  |  |  |
| GEARBOX (If Applicable) |
| 22 | If gearbox is wrapped, check that wrapping and butylmastic paste is securely fastened and that entire gearbox has been wrapped |  |  |  |  |
| 23 | Inspect gearbox cover plate fasteners and ensure they are tight with zero lubrication leakage. Assess where possible if gearbox is wrapped |  |  |  |  |
| 24 | Check that gearbox to valve body fasteners is secure. Assess where possible if gearbox is wrapped |  |  |  |  |
| 25 | Check hand-wheel incorporates freely rotating handle |  |  |  |  |
| 26 | Check the gearbox ratio complies with SPS defined values |  |  |  |  |
| 27 | Check that a gear-driven clock type position indicator is installed on gearbox |  |  |  |  |
| 28 | Check indicator gears are machine cut and mated |  |  |  |  |

| 4. TEST | PASS | FAIL | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| 1 | Open and close the valve via the hand-wheel / cap (request for valve key) or electric actuator if installed and ensure seating is correct |  |  |  |  |
| 2 | Open and close the valve and ensure direction is correct |  |  |  |  |
| 3 | Confirm that open / close indication is correct |  |  |  |  |
| 4 | Open and close the valve. Check that valve opening / closing convention complies with Water Corporation standards (i.e. ACW close, CW open). Note the direction of rotation arrow shall be cast in hand-wheel |  |  |  | Direction of rotation to close: Anti-clockwise Clockwise |

| 5. REMARKS / REMEDIAL / FOLLOW UP ACTIONS | ACTION BY | TARGET DATE | STATUS |
| --- | --- | --- | --- |

| 6. MECHANICAL SIGNOFFS |
| --- |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |

| 7. COATINGS INSPECTION | YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| 1 | Verify coating system and specification ensuring that product is approved for purpose. Confirm internal coating is potable water approved. |  |  |  |  |
| 2 | Consider if ambient conditions are acceptable for holiday testing. Surface temperature should be least 3ºC above dew point and relative humidity less than 85 % before testing. Surface dry and clean for holiday testing. |  |  |  |  |
| 3 | Check internal coating type and verify in accordance with relevant specification (circle D1: Epoxy Coating on Steel/Cast Iron or state, A1: Surface Preparation. |  |  |  | A1/ D1 / OTHER _____________ |
| 4 | Conduct ²dry film thickness (DFT) measurements in at least 10 locations and record values in tables below. |  |  |  |  |
| 5 | Visually inspect condition of internal and external coating appearance including uniformity, colour and free from runs, sags, and inclusions. |  |  |  |  |
| 6 | Carry out spark test on internal coating in accordance to AS/NZS 3894.1 Continuity testing of non-conductive coating – High Voltage (brush) method. Specify voltage at which test is carried out. |  |  |  | Test Voltage: V Pass Fail |
| 7 | Carry out spark test on external coating accordance to AS/NZS 3894.1 Continuity testing of non-conductive coating – High Voltage (brush) method. Specify voltage at which test is carried out. |  |  |  | Test Voltage: V Pass Fail |
| 8 | Valve passes coating condition assessment in accordance with a forementioned tests and inspection. |  |  |  |  |

Refer to AS/NZS 1627 series for Metal Finishing – Preparation and Pre-treatment of Surfaces

2 Refer to AS/NZS 3894.3 methods for Determination of Dry Film Thickness

| 7a. INTERNAL INSPECTION (Microns - DFT) |
| --- |
| NUMBER OF READS (10) | HIGH | LOW | AVERAGE |
| Comments |  |

| 7b. EXTERNAL INSPECTION (Microns - DFT) |
| --- |
| NUMBER OF READS (10) | HIGH | LOW | AVERAGE |
| Comments |  |

| 7c. FLANGE INSPECTION (Microns - DFT) |
| --- |
| NUMBER OF READS (10) | HIGH | LOW | AVERAGE |
| Comments |  |

| 7d. REMARKS / REMEDIAL / FOLLOW UP ACTIONS | ACTION BY | TARGET DATE | STATUS |
| --- | --- | --- | --- |

| 7e. COATING SIGNOFFS |
| --- |
| SUPPLIER NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |

POST TRANSPORTATION INSPECTION

- Inspection to be completed at point of delivery

- If a supply verification was not completed at the manufacturer, both supply verification and post transportation inspection should be completed at point of delivery.

| 8. POST TRANSPORTATION REMARKS / REMEDIAL / FOLLOW UP ACTIONS | ACTION BY | TARGET DATE |
| --- | --- | --- |

| 9. DELIVERY SIGNOFFS |
| --- |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |