- All ITR documents to be completed & witnessed by competent person/s

- Compliance to be achieved to contract requirements and all latest versions of applicable standards

| 1. REFERENCE INFORMATION |
| --- |
| INSPECTION DATA | ASSET DATA |
| PROJECT NAME: | MANUFACTURER: |
| LOCATION: | MF SERIAL NO: |
| INSPECTION DATE: | WC FLER / TAG NO: |
| INSPECTOR NAME: | TYPE / MODEL NO / SIZE: |
| PROJECT / CONTRACT NO: | DESIGN CRITERIA: |
| ATTENDEES: |

| 2. INSPECTION PREPARATION |
| --- |
|  | OSH compliance requirements. |
|  | Obtain QA / QC documentation (review outstanding items). |
|  | Relevant Water Corporation standards. |
|  | Relevant Australian Standards. |
|  | Supporting contract documentation / approved drawings. |
|  | Provision of required test equipment. |
|  | Provision of required test reports and certificates; i.e. hydrostatic test, material certificates, etc. |

| 3. INSPECTION | YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| GENERAL |
| 1 | Visually inspect penstock installation and verify correct installation as per manufacturer’s recommendations |  |  |  |  |
| 2 | Confirm that penstock location is correct as per drawings |  |  |  |  |
| 3 | Verify correct orientation / direction of flow for installed penstock |  |  |  |  |
| 4 | Check that the penstock hand-wheel / cap is accessible and at correct height above floor |  |  |  | Height of hand-wheel / cap: __________________mm |
| 5 | Check that mating flanges are flat, clean and free of irregularities |  |  |  |  |
| 3. INSPECTION | YES | NO | N/A | COMMENTS/DETAILS |
| 6 | Verify gasket material and thickness |  |  |  | Material: CMF EPDM Other _____________________ Thickness: _________________mm |
| 7 | Confirm all bolts installed on penstock and that bolt sizes, material and grade are correct |  |  |  | Size: ________ Material: __________ Grade: 4.6 8.8 Other: _______ |
| 8 | Confirm that associated nut grade is correct |  |  |  | Grade: 5 8 Other __________ |
| 9 | Confirm correct protrusion of bolt threads past nut |  |  |  | Protrusion: _____________________ |
| 10 | Confirm correct bolt tightening sequence has been followed |  |  |  |  |
| 11 | Verify bolt torque requirements comply with DS-38. Also verify actual bolt torque applied to each bolt is correct |  |  |  | DS38 bolt torque: _____________Nm Actual bolt torque: _____________Nm |
| 12 | Verify that torque wrench / machine used is calibrated |  |  |  | Calibration certificate date: _________ |
| 13 | Check that earth ring(s) have been installed correctly |  |  |  |  |
| 14 | Verify that bonding link(s) have been installed correctly |  |  |  |  |
| ISOLATING JOINTS (IF REQUIRED FOR DISSIMILAR METALS OR CATHODIC PROTECTION ISOLATION) |
| 15 | Check that correct isolating bolt sleeves and washers have been installed |  |  |  |  |
| 16 | Verify that a test post has been installed |  |  |  |  |
| 17 | Confirm if a surge diverter has been installed |  |  |  |  |

| 4. TEST | YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| APPLIES TO MANUAL PENSTOCKS AND MANUAL OVERIDE OF ELECTRICALLY ACTUATED PENSTOCKS |
| 1 | Confirm that the penstock starting position is closed. Close the penstock if not already so |  |  |  |  |
| 2 | Slowly open the penstock to fully open and confirm smooth penstock operation during opening and that the required force to open the penstock is not excessive |  |  |  |  |
| 3 | Confirm that the penstock open position indication is correct when in the fully open position |  |  |  |  |
| 4 | Slowly close the penstock to fully closed and confirm smooth penstock operation during closure and that the required force to close the penstock is not excessive |  |  |  |  |
| 5 | Verify the direction of rotation to close |  |  |  | Direction of rotation to close: Anti-clockwise Clockwise |
| 6 | Count the number of turns between fully open and fully closed |  |  |  | Number of turns: ________________ |
| 7 | Confirm that the penstock closed position indication is correct when in the fully closed position |  |  |  |  |

| 5. COATINGS INSPECTION | YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| 1 | Check that penstock internal coating is free of damage |  |  |  |  |
| 2 | Check that penstock external coating is free of damage |  |  |  |  |
| 3 | Confirm that penstock wrapping is satisfactory (buried service only) |  |  |  |  |

| 6. REMARKS / REMEDIAL / FOLLOW UP ACTIONS | ACTION BY | TARGET DATE | STATUS |
| --- | --- | --- | --- |

| 7. SIGNOFFS |
| --- |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |