- All ITR documents to be completed & witnessed by competent person/s

- Compliance to be achieved to contract requirements and all latest versions of applicable standards

| 1. REFERENCE INFORMATION |
| --- |
| INSPECTION DATA | ASSET DATA |
| PROJECT NAME: | MANUFACTURER: |
| LOCATION: | MF SERIAL NO: |
| INSPECTION DATE: | WC FLER / TAG NO: |
| INSPECTOR NAME: | TYPE / MODEL NO / SIZE: |
| PROJECT / CONTRACT NO: | DESIGN CRITERIA: |
| ATTENDEES: |

| 2. INSPECTION PREPARATION |
| --- |
|  | OSH compliance requirements. |
|  | Obtain QA / QC documentation (review outstanding items). |
|  | Relevant Water Corporation standards. |
|  | Relevant Australian Standards. |
|  | Supporting contract documentation / approved drawings. |
|  | Provision of required test equipment. |
|  | Provision of required test reports and certificates; i.e. hydrostatic test, material certificates, etc. |

| 3. INSPECTION | YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| GENERAL |
| 1 | Inspect valve installation and verify installation as per manufacturer’s recommendations |  |  |  |  |
| 2 | Confirm that valve location is correct as per drawings |  |  |  |  |
| 3 | Verify correct orientation / direction of flow for installed valve |  |  |  |  |
| 4 | Check that the valve assembly is accessible and at correct height above floor |  |  |  |  |
| INSTALLATION |  |  |  |  |
| 5 | Confirm there is no “cross threading” of connections |  |  |  |  |
| 6 | Confirm flange or thread connections are free of leaks if possible |  |  |  |  |
| 7 | Confirm manual operators are installed if applicable |  |  |  |  |
| 8 | Verify gasket material and thickness |  |  |  | Material: CMF EPDM Other _____________________ Thickness: _________________mm |
| 9 | Confirm all bolts installed on valve and that bolt sizes, material and grade are correct |  |  |  | Size: ________ Material: __________ Grade: 4.6 8.8 Other: _______ |
| 10 | Confirm that associated nut grade is correct |  |  |  | Grade: 5 8 Other __________ |
| 11 | Confirm correct protrusion of bolt threads past nut |  |  |  | Protrusion: _____________________ |
| ELECTRICAL |
| 12 | Confirm electrical connections (inclusive of earthing) are correct |  |  |  |  |
| 13 | Confirm surge suppression to limit voltage spikes is installed |  |  |  |  |
| 14 | Confirm electrical tags/wiring labels are correct |  |  |  |  |

| 4. TESTING | YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| 1 | Confirm point to point testing correct |  |  |  |  |
| 2 | Confirm earthing correct |  |  |  |  |
| 3 | Confirm supply voltage correct |  |  |  |  |
| 4 | Verify failure position of valve is fail safe |  |  |  |  |

| 5. COATINGS INSPECTION (Not Applicable) | YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |

| 6. REMARKS / REMEDIAL / FOLLOW UP ACTIONS | ACTION BY | TARGET DATE | STATUS |
| --- | --- | --- | --- |

| 7. SIGNOFFS |
| --- |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |