- All ITR documents to be completed & witnessed by competent person/s

- Compliance to be achieved to contract requirements and all latest versions of applicable standards

| 1. REFERENCE INFORMATION |
| --- |
| INSPECTION DATA | ASSET DATA |
| PROJECT NAME: | MANUFACTURER: |
| LOCATION: | MF SERIAL NO: |
| INSPECTION DATE: | WC FLER / TAG NO: |
| INSPECTOR NAME: | TYPE / MODEL NO / SIZE: |
| PROJECT / CONTRACT NO: | DESIGN CRITERIA: |
| ATTENDEES: |

| 2. INSPECTION PREPARATION |
| --- |
|  | OSH compliance requirements. |
|  | Obtain QA / QC documentation (review outstanding items). |
|  | Relevant Water Corporation standards. |
|  | Relevant Australian Standards. |
|  | Supporting contract documentation / approved drawings. |
|  | Provision of required test equipment. |
|  | Provision of required test reports and certificates; i.e. hydrostatic test, material certificates, etc. |

| 3. INSPECTION | YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
| GENERAL |
| 1 | Inspect valve installation and verify installation as per manufacturer’s recommendations |  |  |  |  |
| 2 | Confirm that valve location is correct as per drawings |  |  |  |  |
| 3 | Verify correct orientation / direction of flow for installed valve |  |  |  |  |
| 4 | Check that the valve assembly is accessible and at correct height above floor |  |  |  |  |
| INSTALLATION and Testing |  |  |  |  |
| 5 | Check isolation valves upstream and downstream valves are open if fitted |  |  |  |  |
| 6 | Check fluid/air connections for leaks |  |  |  |  |
| 7 | Check normal position of valve normally closed (NC) normally open NO |  |  |  |  |
| 8 | Manually actuate solenoid valve to check operation |  |  |  |  |
| 9 | Check solenoid valve returns to normal position when returned to auto. |  |  |  |  |
| 10 | Remotely actuate solenoid from control circuit to check operation of solenoid |  |  |  |  |
| 11 | Check solenoid coil for overheating |  |  |  |  |
| ELECTRICAL (to be completed by electrical personnel) |
| 12 | Check all electrical connections |  |  |  |  |
| 13 |  |  |  |  |  |

| 5. COATINGS INSPECTION (Not Applicable) | YES | NO | N/A | COMMENTS/DETAILS |
| --- | --- | --- | --- | --- |
|  | Check external coatings are not damaged |  |  |  |  |

| 6. REMARKS / REMEDIAL / FOLLOW UP ACTIONS | ACTION BY | TARGET DATE | STATUS |
| --- | --- | --- | --- |

| 7. SIGNOFFS |
| --- |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |
| NAME (PRINT) | COMPANY / ROLE | SIGNATURE | DATE |